# Mission 2 Demo and Explanation: Object Detection.py
1. Conversion to Grayscale and Thresholding:
  1. The image is first converted from RGBA to grayscale.
  2. A binary threshold is applied to create a binary image where pixel values are either 0 or 255.
2. Color Segmentation:
  1. The image is converted to the HSV color space for more effective color segmentation.
  2. A mask is created to filter out pixels that fall within the specified HSV range, targeting a specific color (greenish-yellow in this case).
3. Contour Detection and Filtering:
  1. Contours are found in the binary mask.
  2. Small contours, which are likely noise, are filtered out based on their area.
4. Object Identification:
  1. For each valid contour, a bounding rectangle is drawn around it.
  2. The centroid of each object is calculated using image moments.
  3. Centroids and sizes of the detected objects are stored in a list.
5. Visualization:
  1. The detected objects are visualized by drawing rectangles around them on a copy of the original image.
  2. The processed image is displayed in a window for verification.
6. Return Detected Objects:
  1. The function returns a list of dictionaries, each containing the centroid and size of a detected object.

Robot Manipulator
1. Convert Pixel to Normalized Image Coordinates:
  1. The pixel coordinates (x, y) are converted to normalized image coordinates using the camera's intrinsic matrix.
  2. The depth value (z) is included to get the correct scale in the camera's 3D space.
2. Scale by Depth:
  1. The normalized coordinates are scaled by the depth (distance from the camera) to get the 3D coordinates in the camera frame.
3. Convert to Homogeneous Coordinates:
  1. The 3D coordinates are converted to homogeneous coordinates by adding a 1. This allows for the application of transformation matrices that include translation.
4. Apply Transformation Matrix:
  1. The transformation matrix, which maps coordinates from the camera frame to the robot base frame, is applied to the homogeneous coordinates.
5. Convert Back to Non-Homogeneous Coordinates:
  1. The resulting coordinates are converted back to non-homogeneous form by dropping the last element (which was added for the homogeneous transformation).
6. Return Base Frame Coordinates:
  1. The final coordinates in the robot base frame are returned.